## Slide 1
Scaffolds
10-Hour Construction Outreach

## Slide 2: Scaffolds
source: www.elcosh.org/NIOSH/John Rekus

## Slide 3: Scaffolds
Lesson Overview
  Competent person
  Basic types of scaffolds
  Scaffold hazards
  Methods of protecting against scaffold hazards
  Employer requirements
NIOSH/John Rekus/elcosh.org

## Slide 4: Competent Person
Oversees assembly, disassembly, inspection, and safe use of scaffolds
Trains all employees who erect, disassemble, move, operate, repair, maintain, inspect, or work on scaffolds
Source: OSHA

## Slide 5: Competent Person
Process for designating an employee as the competent person:
  Employer appointed
  Capability to identify hazards
  Executes qualified person design
  Authority to take prompt corrective action

## Slide 6: Basic Types of Scaffolds
Suspended
Supported
Aerial lifts
Source: OSHA

## Slide 7: Hazards Associated with Scaffolds
Falls
Falling object(s)
Electrical hazards
Collapse hazards
Planking hazards
Weather conditions
Collisions or struck-by
Source: OSHA

## Slide 8: Reducing and Eliminating Hazards
Proper access
Guardrails
Personal Fall Arrest System (PFAS)
Protection from falling objects
Protection from electrical hazards
Precautions for moving scaffolds
Safe scaffold construction and disassembly

## Slide 9: Proper Access
Required when platforms are more than two feet above or below a point of access
Examples of permitted access - ladders, stair towers, ramps, walkways
Do not use crossbraces or
unapproved ladder-like ends for access
Source: OSHA

## Slide 10: Guardrails
Must be installed on open sides and ends of scaffolds
If front edge (working edge) is more than 14 inches from work, guardrail and/or PFAS system must be used
Source: OSHA

## Slide 11: Guardrails
Toprails
  Supported scaffolds manufactured or placed in service after 1/1/2000 must be 38-45” above platform
Midrails
  When used
  Halfway between toprail and scaffold platform
  Crossbracing, when used as a toprail or midrail, must meet certain height requirements

## Slide 12: Personal Fall Arrest System (PFAS)
Components
Selection of fall protection
Engineering or qualified person design
When to inspect
Free-fall limit
Source: OSHA

## Slide 13: Protection From Falling Objects
Protection must be provided when there is potential of being struck by falling objects
Methods of protection
– Barricades, toeboards, screens
or paneling, canopy or mesh nets, placement of large, heavy objects
Wear a hardhat when working around or below scaffolds
Source: OSHA

## Slide 14: Protection From Electrical Hazards
Minimum distance based on voltage
  Insulated lines
  Uninsulated lines
When exceeding minimum distance as necessary to perform work, utility company must be notified to
  De-energize or relocate line
OR
  Install protective coverings to prevent contact
Source: OSHA

## Slide 15: Moving Scaffolds
Workers may only be on moving scaffold when
  Level ground surface
  Height to width ratio
  Outriggers installed on both sides
  Standing inside the wheel base
  Competent person onsite
Source: OSHA

## Slide 16: Safe Scaffold Construction and Disassembly
Appropriate scaffold construction methods
Provide proper scaffold access
Use a competent person
Manufacturers’ instructions
Source: OSHA

## Slide 17: Employer Requirements
Comply with OSHA standards related to scaffolds
  Training
  Inspection
  Designating competent person
Comply with manufacturers’ requirements and recommendations
Follow plans designed by qualified person

## Slide 18: Scaffold Hazard Recognition
Identify hazards and solutions
Source: www.elcosh/org/OTI/Southwest Education Center

## Slide 19: Scaffold Hazard Recognition
Identify hazards and solutions
Source: www.elcosh/org/OTI/Southwest Education Center

## Slide 20: Scaffold Hazard Recognition
Identify hazards and solutions
Source: www.elcosh/org/OTI/Southwest Education Center

## Slide 21: Scaffold Hazard Recognition
Identify hazards and solutions
Source: www.elcosh/org/OTI/Southwest Education Center

## Slide 22: Scaffold Hazard Recognition
Identify hazards and solutions
Source: www.elcosh/org/OTI/Southwest Education Center

## Slide 23: Always Remember
Employers must
  Designate a competent person for scaffold
  Ensure that employees are trained in proper assembly, disassembly, and use of scaffolds
  Utilize strategies to prevent and reduce scaffold hazards
www.elcosh.org/Steve Clark/Laborers

## Slide 24: Knowledge Check
Who trains employees that work on scaffolds?
  Employees do not need training
  Employees are responsible for their own training
  Fellow employees who have experience
  Employer-designated competent person
d. Employer-designated competent person

## Slide 25: Knowledge Check
Scaffolds must be designed by a .
  Competent person
  Construction site manager
  Qualified person
  Experienced scaffold worker
c. Qualified person

## Slide 26: Knowledge Check
Which of the following is NOT an example of proper access?
  Ladders
  Crossbraces
  Stair towers
  Walkways
b. Crossbraces