## Slide 1
Fall Protection
OSHA 10-hour Outreach Training General Industry

## Slide 2: Introduction
Fatal Fall
Eighteen-Year-Old Sporting Goods Retail Store Worker Dies in a Fall From a Shelving Unit - Pennsylvania
NIOSH In-house FACE Report 2001-06

## Slide 3: Introduction
Slips, trips, and falls make up the majority of general industry accidents
Are second only to motor vehicle crashes

## Slide 4: Introduction
Unless working on a ladder, scaffold or scissor lift, OSHA requires fall protection when exposed to a
4-foot fall or greater.
Source: OSHA

## Slide 5: Introduction
Lesson Objectives
Identify types of fall hazards associated with workplace environments.
Identify methods to eliminate or protect against fall hazards.

## Slide 6: Common Fall Hazards
Overhead Platforms
Overhead Runways
Elevated Work Stations
Source of photos: OSHA

## Slide 7: Common Fall Hazards
Floor Openings/Pits
Wall Openings
Shelving Units
Source of photos: OSHA

## Slide 8: Common Fall Hazards
Stationary Storage Tanks
Tanker Trucks
Industrial Production Units
Source: WVU
Source: OSHA
Source: OSHA

## Slide 9: Fall Hazard Controls
Hierarchy of Fall Hazard Control:
First line of defense
  Eliminate the fall hazard
Second line of defense
  Prevent the fall
Third and last resort
  Control the fall

## Slide 10: Fall Hazard Controls
Source: WVU
Eliminate fall hazards
– work from the ground
Gauge at top of tank moved to ground level
Use drone, equipped with camera, for inspections at heights

## Slide 11: Fall Hazard Controls
Source: WVU
Eliminate fall hazards – hole covers/grates
Very effective way to eliminate a fall hazard.
Designed to withstand intended load.
Secured-bolted, hinged, latched, locked

## Slide 12: Fall Hazard Controls
Source: OSHA
Prevent the fall – guardrails
Standard railing
  Top rail, mid rail, and posts
  Height from upper surface of top rail to floor level is 42” (+/− 3”)
  Mid-rail height is 21”
Standard toeboard
  3.5” high
  Not more than ¼” clearance above the floor

## Slide 13: Fall Hazard Controls
Source: WVU
Prevent the fall – fences and barricades
Prevents unauthorized employee exposure to fall hazard
Employer authorizes access
Authorized personnel must then be protected from the fall hazards within

## Slide 14: Fall Hazard Controls
Source: OSHA
Prevent the fall –
personal all restraint
Prevent falls by keeping worker from reaching fall hazard
Comprised of a body belt or body harness, an anchorage, connectors
Often used when section of guardrail or hole cover is temporarily removed

## Slide 15: Fall Hazard Controls
Source: Honeywell/Miller; used with permission.
Know the A, B, Cs of Personal Fall Arrest Systems
Anchorages
Body harness
Components
(connectors like snaphooks or Dee-rings, connection points, lanyards, deceleration devices,
lifelines, etc.)
Installed, used, and maintained according to the manufacturer

## Slide 16: Fall Hazard Controls
PFAS – temporary anchorage

## Slide 17: Fall Hazard Controls
PFAS – permanent anchorage

## Slide 18: Fall Hazard Controls
PFAS – full-body harness

## Slide 19: Fall Hazard Controls
PFAS – connecting components

## Slide 20: Fall Hazard Controls
Source: OSHA
Control the fall –
positioning devices
Consists of a body belt and connecting device
Keeps workers from falling, while allowing their hands to be free to perform work

## Slide 21: Fall Hazard Controls
Source: OSHA
Control the fall –
safety net systems
Consists of specially designed mesh nets, panels, and connecting components
Must be designed, installed and maintained properly

## Slide 22: Employer Requirements
Training – your employer must train you on the following:
Fall hazards associated with your facility and your work
Methods used to protect you from those hazards
Proper and safe use of any personal fall arrest, positioning, or fall restraint systems
Applicable OSHA standards

## Slide 23: Employer Requirements
Inspection
Your employer must inspect the:
  workplace for existing and potential fall hazards
  fall hazard controls used; such as guardrails, covers, grates, and anchorage points
You must inspect your PFAS, Positioning and Fall Restraint hardware before each use.

## Slide 24: Employer Requirements
Source: OSHA
Rescue
Personal Fall Arrest Systems require a rescue plan
Employer must develop and communicate the rescue plan to all involved

## Slide 25: Hazard Recognition
Source of photo: OSHA

## Slide 26: Hazard Recognition
Source of photo: OSHA

## Slide 27: Hazard Recognition
Source of photo: OSHA

## Slide 28: Hazard Recognition
Source of photo: OSHA

## Slide 29: Knowledge Check
What is the first line of defense when it comes to falls in the workplace?
  Control the fall itself once it occurs
  Eliminate the fall hazard completely
  With the fall hazard present, prevent the fall.
  Use personal protective equipment
Answer: b. Eliminate the fall hazard completely

## Slide 30: Knowledge Check
A worker is required to remove a section of guardrail in order to receive materials from a fork truck; which of the following provides the best protections to prevent a fall?
  Avoid the edge
  Use a personal fall arrest system
  Use a fall restraint system
  Use grab handles
Answer: c. Use a fall restraint system

## Slide 31: Knowledge Check
A personal fall arrest system (PFAS) anchorage point must be capable of handling pounds.
  2,000
  3,000
  4,000
  5,000
Answer: d. 5,000