## Slide 1
Materials Handling, Storage, Use, and Disposal
OSHA 10-hour Outreach Training General Industry

## Slide 2: Introduction
Lesson objectives:
Identify types of material handling equipment.
Describe hazards associated with material handling activities.
Identify methods to prevent hazards associated with material handling equipment.
Recognize employer requirements to protect workers from material handling hazards.

## Slide 3: Types of Equipment
Conveyors
Source: TEEX-Harwood
Source: OSHA
Powered Industrial Trucks

## Slide 4: Types of Equipment
Cranes
Slings
Source: TEEX
Source: OSHA

## Slide 5: Hazards Associated with Materials Handling
Factors contributing to injuries:
Weight and bulkiness of objects
Bending, twisting, turning movements
Source of photos: OSHA

## Slide 6: Hazards Associated with Materials Handling
Hazards:
Improper operation of equipment
Accumulated materials or clutter
Source: OSHA

## Slide 7: Hazards Associated with Materials Handling
Unsafe conditions of materials or containers
Flammability or toxicity of some materials
Source: OSHA

## Slide 8: Hazards Associated with Materials Handling
Weight of materials
Binding ties or other devices that secure bundles or
bound materials
Source: OSHA

## Slide 9: Hazards Associated with Materials Handling
Falling objects
Lifting, pushing, pulling, or otherwise manually moving large, heavy items
Source: OSHA
Source: OSHA

## Slide 10: Hazards Associated with Materials Handling
Improperly stacked materials
Struck-by or caught-in/-between hazards
Source TEEX - Harwood
Source: OSHA

## Slide 11: Hazards Associated with Materials Handling
Types of injuries commonly reported:
Sprains, strains, tears
Soreness and pain
Bruises and contusions
Cuts, lacerations, punctures, crushing, and amputations
Source: OSHA

## Slide 12: Hazards Associated with Materials Handling
Examples of events or exposures leading to injuries:
Contact with objects and equipment
Transportation incidents
Exposure to harmful substances or environments
Source: OSHA
Source: OSHA

## Slide 13: Hazards Associated with Materials Handling
Falls, slips, trips, or loss of balance
Repetitive motion
Overexertion
Source: OSHA
Source: OSHA

## Slide 14: Preventing Hazards
Moving materials manually:
Use devices to assist with holding loads
Wear PPE
Use proper lifting technique
Seek help for oversized loads
Use blocking materials
Source of photos: OSHA

## Slide 15: Preventing Hazards
Overhead and gantry cranes:
Never move a load over co-workers or allow co-workers to walk underneath
Return the load block to its designated
location after use
Do not leave the load
block low enough for someone to run into
Never leave a suspended load unattended
Source: OSHA

## Slide 16: Preventing Hazards
Do not leave unused slings suspended on a crane hook
Store wall-mounted cranes against the wall
Continuously observe equipment for any sign of problems during operation.
Don’t allow yourself to become distracted.

## Slide 17: Preventing Hazards
Operated only by thoroughly trained and qualified workers
Source: UA

## Slide 18: Preventing Hazards
Eliminate/reduce crane hazards by:
Knowing
  Load
  Capacity of the crane
  When the load is safe to lift
Always checking crane load chart and never exceed load limits
Source: TEEX - Harwood
Source: TEEX - Harwood

## Slide 19: Preventing Hazards
Inspection of crane by a qualified person
  Modified, repaired, or adjusted
  Post-assembly
  At least every 12 months
  Equipment not in regular use
Visual inspection by a competent person
  Prior to each shift
  Monthly
Source: OSHA

## Slide 20: Preventing Hazards
Slings
  Connects a crane hook to a load
  Proper selection
  Inspection
Source of photos: OSHA

## Slide 21: Preventing Hazards
Reduce sling hazards by:
  Lubricating
  Not shortening with knots, bolts, or other devices, or kink legs
  Keeping clear of loads
  Avoiding sudden movement

## Slide 22: Preventing Hazards
Forklifts
Main causes of injuries
  Forklift overturns
  Forklift striking workers on foot
Persons crushed by forklifts
Persons falling from forklifts
Forklift toppled sideways possibly due to shift in center of gravity.
Source: OSHA

## Slide 23: Preventing Hazards
Illegal forklift operators
  Anyone under 18
  Anyone not properly trained
Source of photos: OSHA

## Slide 24: Preventing Hazards
Driving the forklift
  Obstructed vision
  Travel path
  Approaching people
  Elevated platform
  Seat belts and ROPS
  Raising/lowering forks
  Safe distance
Source of photos: OSHA

## Slide 25: Preventing Hazards
Elevating workers with forklift
  Standing on forks
  Lifting personnel
  Approved lift platform
  Restraining means
Source: OSHA

## Slide 26: Preventing Hazards
Driving forklift on grades/ramps
  Use extreme caution
  No turns
  Tilting and raising load
  Point load up the incline
Source of photos: OSHA

## Slide 27: Preventing Hazards
Forklift operating speed
  Tip-overs
  Turning
  Avoiding collisions
  Wet and slippery floors
  Ascending/descending
  Obstructed vision
Source of photos: OSHA

## Slide 28: Preventing Hazards
Avoiding excess weight
  Do not exceed weight capacity of forklift.
  Center loads and secure to keep from shifting to maintain balance of weight
Source of graphics: OSHA

## Slide 29: Preventing Hazards
Use of dock boards for loading/uploading
  Bridging space
  Securing portable dock boards
  Handholds for dock boards
Source: OSHA

## Slide 30: Preventing Hazards
Exiting the forklift
  Set brake, lower forks/lifting carriage, neutralize controls
  Stand-up type forklift
Riding the forklift
  No passengers allowed
  Exception – seat is provided
Source of photos: OSHA

## Slide 31: Preventing Hazards
Avoiding struck-by/crushed-by
  Don’t jump from an overturning, sit-down type forklift.
  Stay with the truck, hold on firmly, and
lean in the opposite direction of the overturn.
Source: OSHA

## Slide 32: Preventing Hazards
Forklift training – do not operate a forklift without proper training
Reporting damage – any damage or problems that occur to a forklift during a shift should be reported to the supervisor.
Source: OSHA

## Slide 33: Employer Requirements
Comply with OSHA standards related to materials handling, including:
Training requirements
Inspection requirements
Source of photos: OSHA

## Slide 34: Employer Requirements
Comply with manufacturers’ requirements and recommendations for materials handling equipment.
Source : OSHA

## Slide 35: Recognizing Hazards
Identify potential hazards and possible solutions:
Source: OSHA

## Slide 36: Recognizing Hazards
Identify potential hazards and possible solutions:
Source: OSHA
Source: TEEX - Harwood

## Slide 37: Recognizing Hazards
Identify potential hazards and possible solutions:
Source of photos : TEEX Harwood
Source of photos : OSHA -UFCW

## Slide 38: Knowledge Check
What is the minimum age requirement for the operation of a forklift, regardless of training?
  16
  18
  21
  25
Answer: b. You must be at least 18 years old to operate a forklift.

## Slide 39: Knowledge Check
A way to prevent materials handling hazards is to .
  refuse to allow personnel to ride equipment without a seat and seatbelt
  report all damaged equipment immediately
  operate within manufacturer’s specifications
  All of these
Answer: d. All of these are good ways to prevent materials handling hazards.

## Slide 40: Knowledge Check
Which of the following is a method for eliminating or reducing crane operation hazards?
  A competent person should visually inspect the crane once a year
  Never exceed the load limit by more than 10%
  Never move a load over co-workers
  All of these
Answer: c. Never move a load over co-workers or allow co-workers to walk underneath.

## Slide 41: Knowledge Check
Employers must comply with OSHA standards related to materials handling, including training and .
  equipment
  operations
  inspection
  all of these
Answer: c. Employers must comply with OSHA standards for training and inspection.