## Slide 1
Hazard Communications
OSHA 10-Hour General Industry Outreach Training

## Slide 2: Introduction
Lesson objectives:
Identify the employer’s responsibilities under the HCS, including training requirements.
Identify components of a Hazard Communication program.
Describe requirements of the different types of Hazard Communication labels.
Locate pertinent information about chemicals on labels, including other forms of hazard communication, to ensure “right to understanding” provisions of GHS requirements.

## Slide 3: Introduction
Case study
Source: OSHA

## Slide 4: Introduction
HCS/GHS
Save lives
  Approximately 43 per year (deaths)
  Approximately 585 per year injuries/illnesses
Save $
  $475.2M in increased productivity
  $32.2M in cost savings

## Slide 5: Introduction
Seven major elements in the GHS-aligned Hazard Communication Standard
Source: OSHA

## Slide 6: Employer Responsibilities
Employer responsibilities under the HCS:
Ensure labels are on incoming labels and not defaced
Maintain SDSs from shipments
Obtain SDSs if not received
Ensure SDSs are readily accessible
Ensure chemicals in workplace are properly labeled, tagged, or marked
Provide information and training to employees
Provide information/access for employees in multi-employer workplaces
Develop, implement, and maintain a written hazard communication program

## Slide 7: Employer Responsibilities
How hazard communication works:
Source: OSHA

## Slide 8: Hazard Communication Program
Requirements for a written program:
Develop, implement, and maintain a written hazard communication program
Main intent is to ensure compliance with standard in a systematic way that coordinates all elements

## Slide 9: Hazard Communication Program
Components of written program:
Lists of hazardous chemicals present at worksite
Availability of SDSs to employees and downstream employers
Labeling of chemical containers
Training programs regarding hazards of chemicals and protective measures

## Slide 10: Hazard Communication Program
List of hazardous chemicals:
Use product identifier
  Product name, common name or chemical name
  Same as name used on SDS and label
Inventory of chemicals – employer must have available an SDS for each
Covers all chemicals in all forms, whether contained or not
Include chemicals in containers, pipes, and those generated by work operations

## Slide 11: Hazard Communication Program
Safety data sheet (SDS):
Available and accessible to workers
Required for all hazardous chemical used
Do not use hazardous chemicals if there is no SDS available
16-section format
Source: OSHA

## Slide 12: Hazard Communication Program
SDS documentation:
Designate person(s) responsible for obtaining and maintaining SDSs
Describe how SDSs are maintained and how employees can access them
Procedures if SDS is not received with first shipment
Must have SDS for each chemical; train workers on SDS format and use
Source: OSHA

## Slide 13: Hazard Communication Program
SDS 16-section format:
Section 1: Identification
Section 2: Hazard(s) identification
Section 3: Composition/information on ingredients
Section 4: First-aid measures
Section 5: Fire-fighting measures
Section 6: Accidental release measures
Section 7: Handling and storage
Section 8: Exposure control/personal protection
Source: OSHA

## Slide 14: Hazard Communication Program
Section 9: Physical and chemical properties
Section 10: Stability and reactivity
Section 11: Toxicological information
Section 12: Ecological information
Not regulated
by OSHA
Section 13: Disposal considerations
Section 14: Transport information
Section 15: Regulatory information
Section 16: Other information

## Slide 15: Hazard Communication Program
Source: OSHA

## Slide 16: Hazard Communication Program
Labeling:
All containers of hazardous materials must be labeled
Immediate warning
Snapshot of hazards and protective information

## Slide 17: Hazard Communication Program
Documentation for labeling:
Designate person(s) responsible for labeling compliance
Describe alternatives to labeling of stationary process containers
Ensure all workplace containers are labeled appropriately
Labels included in training (shipping and workplace containers)
Procedures for reviewing/updating workplace label information

## Slide 18: Hazard Communication Program
Required elements for shipping labels:
Name, address, telephone number
Product identifier
Signal word
Hazard statement(s)
Precautionary statement(s)
Pictogram
This sample illustrates the required elements for shipping labels. Source: OSHA

## Slide 19: Hazard Communication Program
Requirements for workplace labels:
Employers can create own labeling system that works for their workplace/employees
Can choose same label required for shipped containers or alternative labels as long as they provide general information about hazards
Train employees to understand
Source: OSHA

## Slide 20: Hazard Communication Program
Training requirements:
Train employees on hazardous chemicals in their work area
– Before initial assignment
When new hazards are introduced
Nonroutine tasks
Include in training
  Methods/observations to determine presence/release of chemical in work area
  Hazards of chemicals
  Appropriate protective measures
  Where and how to obtain additional information
Source: OSHA

## Slide 21: Hazard Communication Labels
Types of labels:
HCS shipping labels
HCS workplace labels
NFPA 704 labels
HMIS labels
DOT shipping labels, placarding, and markings
Source of graphics: OSHA

## Slide 22: Hazard Communication Labels
Required elements for HCS shipping labels:
Product identifier
Signal word
Hazard statement(s)
Precautionary statement(s)
Pictogram
Name, address, telephone number
Source: OSHA

## Slide 23: Hazard Communication Labels
How the hazardous chemical is identified
Contact information of Responsible Party
Source: OSHA

## Slide 24: Hazard Communication Labels
Indicates the relative level of severity of hazard;
“Danger” is used for more severe hazards and “Warning” for less severe hazards
Pictograms convey specific information about the hazards of a chemical in symbols and other graphic elements
Source: OSHA

## Slide 25: Hazard Communication Labels
Exclamation Mark
Source: OSHA

## Slide 26: Hazard Communication Labels
Exploding Bomb
Source: OSHA

## Slide 27: Hazard
Communication Labels
Not regulated by OSHA
Skull and Crossbones
Source: OSHA

## Slide 28: Hazard Communication Labels
Statement assigned to hazard class and category that describes the nature of the hazard(s), of a chemical, including, where appropriate, the degree of hazard.
Describes recommended measures that should be taken to minimize or prevent adverse effects resulting from exposure to a hazardous chemical, or improper storage or handling.
Source: OSHA

## Slide 29: Hazard Communication Program
Requirements for workplace labels:
Same information as label from manufacturer or product identifier and words, pictures, symbols or combination thereof
May include signs, placards, process sheets, batch tickets, operation procedures, other written materials
Source of graphics: OSHA

## Slide 30: Hazard Communication Labels
Alternative workplace labels:
  Permitted for workplace labels
  Must provide at least general information regarding hazards of chemicals
  Hazard warnings or pictograms that conflict
with HCS label elements cannot be used
  Examples: NFPA 704 and HMIS
Source: OSHA
Source: TEEX

## Slide 31: Hazard Communication Labels
Other labels:
NFPA 704
  Overall diamond shape made up of four smaller diamonds
  Each smaller diamond is a different color
  Numbers within smaller diamonds represent severity of hazard
Source: OTIEC

## Slide 32: Hazard Communication Labels
azard
y
nstability
Hazard
Health
Hazard
Other
Special
Hazard
– NFPA 704 – hazards and severity ratings
0= normal material that
poses no health
I 1 = slight hazard
2 = moderate hazard
3 = extreme hazard
4 = deadly hazard
Red = Flammability Hazards
0= will not burn
1 = flashpoint above 200°F
2 = flashpoint between 100 – 200°F
3 = flashpoint below 100°F
4 = flashpoint less than 73°F
Flam
H
Yellow = Instability Hazards
0= normally stable
1 = slight hazard
2 = moderate hazard
3 = extreme hazard
4 = deadly hazard
White = Other Special Hazards mabilit Blue = Health Hazards
W= reactivity to water
OX = oxidizer
SA = simple asphyxiant
Source: OTIEC

## Slide 33: Hazard Communication Labels
Source: OSHA

## Slide 34: Hazard Communication Labels
HMIS label
  Intended for “In-plant” (workplace) labeling compliance
  Color-coded bars
  Numerical scale, 0-4, with 0 as lowest hazard and 4 as highest hazard
    0 = minimal hazard
    1 = slight hazard
    2 = moderate hazard
    3 = serious hazard
    4 = severe hazard
(Product identifier)
HEALTH
FLAMMABILITY
PHYSICAL HAZARD
PERSONAL PROTECTION
Source: OTIEC

## Slide 35: Hazard Communication Labels
HMIS hazard indicators
(Product identifier)
HEALTH
FLAMMABILITY
PHYSICAL HAZARD
PERSONAL PROTECTION
Health ratings:
0 = no significant risk
1 = irritation/minor injury
2 = temporary/minor injury
Source: OTIEC
Health ratings:
The second space signifies chronic health hazard with an asterisk (*)
3 = major injury
4 = life-threatening
but <200°F
3 = flashpoint <73°F and boiling point >100°F, or flashpoint between 73°F and 100°F
4 = flashpoint <73°F and
boiling point <100°F
Flammability ratings:
0 = will not burn
1 = flashpoint >200°F
2 = flashpoint ≥100°F,
Physical Hazard ratings:
0 = normally stable
1 = normally stable, but
can become unstable
2 = unstable
3 = explosive
4 = readily explosive
PPE Index:
A = safety glasses
B = safety glasses + gloves
C = safety glasses + gloves + apron
D = face shield + gloves + apron
E = safety glasses + gloves + dust
respirator
F = safety glasses + gloves + apron
+ dust respirator
G = safety glasses + gloves + vapor
respirator
H = splash goggles + gloves + apron
+ vapor respirator
I = safety glasses + gloves + dust and vapor respirator
J = splash goggles + gloves + apron
+ dust and vapor respirator
K = air-line hood or mask + gloves +
full suit + boots
X = ask supervisor or safety specialist
(Product identifier)

## Slide 36: Hazard Communication Labels
Ammonium Hydroxide |  | 
HEALTH | * | 2
FLAMMABILITY |  | 0
PHYSICAL HAZARD |  | 0
PERSONAL PROTECTION |  | J
Source: OTIEC

## Slide 37: Hazard Communication Labels
DOT shipping containers – marking, labeling, and placarding
  Uses graphic elements on square-on-point placards or labels to identify shipments of hazardous materials
  Square-on-points have backgrounds of various colors
  Where shipping container is also container used in workplace, workers must be made aware of DOT pictograms
  DOT Classification – groups hazardous materials
based on dangers posed in transportation; 9 classes

## Slide 38: Hazard Communication Labels
Labels
Placards
Markings
Source: OSHA
Source: TEEX
Source: DOT - PHMSA

## Slide 39: Hazard Communication Labels
DOT
Warning
Labels
Source: DOT - PHMSA

## Slide 40: Hazard Communication Labels
DOT
Warning Placards
Source: DOT - PHMSA

## Slide 41: Hazard Communication Labels
DOT Markings
Source: DOT - PHMSA

## Slide 42: Locating Information
Source: OSHA

## Slide 43: Locating Information
Source: OSHA

## Slide 44: Locating Information
Source: OSHA

## Slide 45: Locating Information
In which section of an SDS would you find the following information:
Hazard identification such as hazard classification, signal word, and precautionary statements Section 2: Hazard(s) Identification
Initial care instructions for untrained responders attending to an individual who has been exposed to the chemical
Section 4: First-Aid Measures
Recommendations for PPE
Section 8: Exposure Controls/Personal Protection

## Slide 46: Summary
In this module we discussed:
Employer’s responsibilities under HCS
Components of a Hazard Communication Program
Requirements of different types of Hazard Communication labels
How to locate pertinent information

## Slide 47: Knowledge Check
A hazard communication program requires which of the following components?
  Written program
  SDS/Labeling
  Training
  All of the Above
Answer: d. All of the above

## Slide 48: Knowledge Check
How many sections are required on an SDS?
  11 sections
  16 sections
  4 sections
  As many as necessary to convey understanding
Answer: b. 16 sections

## Slide 49: Knowledge Check
Which of the following statements is true of the pictograms on HCS labels?
  Pictograms on HCS labels are identical to those used on DOT transport labels and may have various background colors.
  Consist of four bars that are color-coded as blue,
red, yellow, and white to match hazard.
  HCS pictograms are required and standardized red square-on-points with black hazard symbols and white backgrounds.
  All of the Above
Answer: c. HCS pictograms are required and standardized red square-on-points with black hazard symbols and white backgrounds.

## Slide 50: Knowledge Check
Your right to understand is .
  not simply shown or told
  not simply given an SDS
  required at initial assignment/when thing change
  all of the above
Answer: d. all of the above