## Slide 1: Machine Guarding
OSHA 10-hour Outreach Training General Industry

## Slide 2: Introduction
Possible machinery-related injuries include:
Crushed fingers or hands
Amputations
Burns
Blindness
A good rule to remember is:
Any machine part, function, or process which may cause injury must be safeguarded.

## Slide 3: Introduction
Lesson objectives:
Identify the main causes of machinery accidents.
Recognize basic machinery parts that expose workers to hazards.
Recognize workplace situations involving machinery that requires guarding.
Identify the requirements for safeguards.
Identify types of machine guards including types of devices used to safeguard machines.

## Slide 4: Machinery Accidents
Examples of how machine accidents can occur:
Reaching-in to “clear” equipment
Not using Lockout/Tagout
Unauthorized persons doing maintenance or using the machines
Missing or loose machine guards

## Slide 5: Machinery Accidents
Amputations:
Unguarded/inadequately safeguarded machinery
Materials handling activities
Activities involving stationary machines
Source: OSHA
Source: OSHA

## Slide 6: Basic Machinery Parts and Hazards
Three fundamental machine areas:
Point of operation
Power transmission device
Operating controls – mechanical or electric power control
Source: OSHA

## Slide 7: Basic Machinery Parts and Hazards
Point of operation:
Where work is performed on material
Examples
  Cutting
  Shaping
  Boring
  Forming
Source: OSHA DTE

## Slide 8: Basic Machinery Parts and Hazards
Power transmission device:
Parts that transmit energy to the part of the machine performing work
Examples
Flywheels
Pulleys
Belts
Connecting rods
Couplings
Cams
Spindles
Chains
Cranks
Gears

## Slide 9: Basic Machinery Parts and Hazards
Hazardous motions and actions:
Motions
  How the machine part moves
  Examples: rotating, in-running nip points, reciprocating, and transversing
Actions
  Operation that the machine part performs
  Examples: cutting, punching, shearing, bending

## Slide 10: Basic Machinery Parts and Hazards
Source of graphics: OSHA
Rotating parts with hazardous projections

## Slide 11: Basic Machinery Parts and Hazards
Source of graphics: OSHA
Common nip points on rotating parts

## Slide 12: Basic Machinery Parts and Hazards
Source of graphics: OSHA
Nip points between rotating elements and parts with longitudinal motions

## Slide 13: Basic Machinery Parts and Hazards
Source of graphics: OSHA
Nip points between rotating machine components

## Slide 14: Basic Machinery Parts and Hazards
Source: OSHA
Reciprocating motions:
  Back-and-forth
  Up-and-down

## Slide 15: Basic Machinery Parts and Hazards
Source of graphics: OSHA
Transverse motion – movement in straight, continuous line

## Slide 16: Basic Machinery Parts and Hazards
Source: OSHA
Cutting action – may involve rotating, reciprocating, or transverse motion

## Slide 17: Basic Machinery Parts and Hazards
Source: OSHA
Punching action – power applied to a slide (ram) for purpose of blanking, drawing, or stamping metal or other materials

## Slide 18: Basic Machinery Parts and Hazards
Source: OSHA
Shearing action – applying power to a slide or knife in order to trim or shear metal or other materials.

## Slide 19: Basic Machinery Parts and Hazards
Source: OSHA
Bending action – applying power to draw or stamp metal or other materials

## Slide 20: Machinery That Requires Guarding
Machines that require point of operation guarding:
Guillotine cutters
Shears
Alligator shears
Power presses
Milling machines
Power saws
Jointers
Portable power tools
Forming rolls and calenders
Source of graphics: OSHA

## Slide 21: Machinery That Requires Guarding
Exposure of fan blades:
  Guard when periphery of blades is less than 7’ above the floor or working level
  Guards with openings no larger than ½”
Source of graphics: OSHA

## Slide 22: Machinery That Requires Guarding
Source of graphics: OSHA
Abrasive wheel machinery:
  Adjustable tongue guard to within ¼” of wheel
  Work rest with maximum opening of 1/8”
  Cover spindle end, nut, flange projections

## Slide 23: Machinery That Requires Guarding
Revolving barrels, containers, and drums:
Guard by an enclosure which is interlocked with drive mechanism
Guards with openings no larger than ½”
Source: OSHA

## Slide 24: Machinery That Requires Guarding
Power-transmission apparatus:
Shafting, flywheels, pulleys, belts, chain drives, etc.
Less than 7 feet from the floor or working platform must be guarded
d belt
Unguarde and pulley
Source: OSHA
Unguarded belt and pulley

## Slide 25: Machinery That Requires Guarding
Machinery associated with amputations – examples:
Mechanical power presses
Power press breaks
Powered and non- powered conveyors
Printing presses
Roll-forming and roll-bending machines
Shearing machines
Food slicers
Meat grinders
Meat-cutting band saws
Drill presses
Milling machines
Grinding machines
13. Slitters
Source of graphics: OSHA

## Slide 26: Requirements for Safeguards
Safeguards must meet these minimum general requirements:
Prevent contact
Be secured
Protect from falling objects
Create no new hazards
Create no interference
Allow safe lubrication
Source: OSHA

## Slide 27: Types of Machine Safe Guards
Safeguarding machinery:
Primary methods
  Guards
  Devices
Ensure employee protection
  Properly designed, constructed, and installed
  Used and maintained in good operating condition

## Slide 28: Types of Machine Safe Guards
Secondary methods
  Probe detection and safety edge devices
  Awareness devices
  Safeguarding methods
    Safe distance
    Safe holding
    Safe opening
  Safe work practices
Safe work procedures
Complementary equipment

## Slide 29: Types of Machine Safe Guards
Guards:
Preferable to other control methods
Provide physical barrier that prevents contact with dangerous machine parts
Four general types
  Fixed
  Interlocked
  Adjustable
  Self-adjusting
Source: OSHA

## Slide 30: Types of Machine Safe Guards
Fixed guard:
Provides a barrier
Permanent part of the machine, preferable to all other types of guards.
Source of photos: OSHA

## Slide 31: Types of Machine Safe Guards
Interlocked guards:
Shuts off or disengages power, stops moving parts, and prevents starting of machine when guard is open
May use electrical, mechanical, hydraulic, or pneumatic power, or combination
Source: OSHA

## Slide 32: Types of Machine Safe Guards
Adjustable guards:
Shuts off or disengages power
Stops moving parts
Prevents starting of machine when guard is open
Source: OSHA

## Slide 33: Types of Machine Safe Guards
Self-adjusting guards:
Openings of barriers determined by movement of the stock
Places barrier between danger area and operator
Source: OSHA

## Slide 34: Types of Machine Safe Guards
Devices:
Controls or attachments that prevent inadvertent access by employees to hazardous machine areas
Examples
Presence sensing
  Photoelectric
  Radiofrequency
  Electromechanical
Pullback
Restraint
Safety trip controls
Two-hand control
Two-hand trip
Gate

## Slide 35: Types of Machine Safe Guards
Presence-sensing devices:
Photoelectric
Radiofrequency
Electromechanical
Source: OSHA

## Slide 36: Types of Machine Safe Guards
Pullback devices:
Utilize a series of cables attached to operator
Automatically withdraws hands from point of operation when slide/ram begins to descend
Source: OSHA

## Slide 37: Types of Machine Safe Guards
Hands in die, feeding
Point of operation exposed
Pullback device attached and properly adjusted
Die closed
Hands withdrawn from point of operation by pullback device
Source: OSHA
Source: OSHA

## Slide 38: Types of Machine Safe Guards
Restraint devices:
Utilize cables/straps attached to operator’s hands and a fixed point
No extending/retracting action involved
Hand-feeding tools may be necessary
Source of graphics: OSHA

## Slide 39: Types of Machine Safe Guards
Safety trip controls:
Deactivates the machine in an emergency situation
Examples
  Pressure-sensitive bar
  Safety tripod
  Safety tripwire
Positioning is critical; must stop machine before body reaches danger area
Source of graphics: OSHA

## Slide 40: Types of Machine Safe Guards
Two-hand controls:
Deactivates the machine in an emergency situation
Pressure-sensitive
Positioning is critical; must stop machine before body reaches danger area
Source of graphics: OSHA

## Slide 41: Types of Machine Safe Guards
Gate devices:
Moveable barrier that protects operator at point of operation before machine cycle can be started
Must be interlocked so machine cannot begin cycle unless gate guard is in place
Must be closed before machine can function
Types
  “A” Gate
  “B” Gate

## Slide 42: Types of Machine Safe Guards
Gate devices:
Gate Open
Moveable barrier that protects operator at point of operation before machine cycle can be started
Must be interlocked so machine cannot begin cycle unless gate guard is in place
Must be closed before machine can function
Source of graphics: OSHA
Gate Closed
Gate Open
Gate Closed

## Slide 43: Types of Machine Safe Guards
Type “A” Gate Operation
Source of graphics: OSHA
Type “B” Gate Operation

## Slide 44: Additional Safeguarding
Location/distance:
The dangerous moving part of a machine must be so positioned that those areas are not accessible or do not present a hazard
Feeding process safeguarded by maintaining safe distance to protect worker
Operator’s controls located safe distance from machine
Source: OSHA

## Slide 45: Additional Safeguarding
Feeding and ejection methods:
Automatic/
semi-automatic feed
Automatic/
semi-automatic ejection
Robots
Transparent Enclosure Guard
Stock Feed Roll
Completed Work
Source of graphics: OSHA

## Slide 46: Additional Safeguarding
Miscellaneous aids:
Awareness barriers
Protective shields
Hand-feeding tools
Source of graphics: OSHA

## Slide 47: Identify the Hazard
Unguarded lower blade and arbor end of radial saw.

## Slide 48: Identify the Hazard
Guard removed from chain rail exposing pins on the spiked chain and sprocket mechanism.

## Slide 49: Summary
Safeguards are essential for protecting workers from needless and preventable machinery-related injuries
The point of operation, as well as all parts of the machine that move while the machine is working, must be safeguarded
A good rule to remember is:
Any machine part, function, or process which may cause injury must be safeguarded

## Slide 50: Knowledge Check
All machines consist of three fundamental areas, including .
  Flywheels, connecting rods, and transverse moving parts
  Point of operation, power transmission device, and operating controls
  Reciprocating parts, rotating parts, and on/off switch
  Feed mechanisms, auxiliary machine parts, and nip points
Answer: b. point of operation, power transmission device, and operating controls

## Slide 51: Knowledge Check
Rotating, in-running nip points, reciprocating, and transversing are types of hazardous .
  motions
  actions
  guards
  devices
Answer: a. motions

## Slide 52: Knowledge Check
Cutting, punching, shearing, and bending are types of hazardous .
  motions
  actions
  guards
  devices
Answer: b. actions

## Slide 53: Knowledge Check
Which of the following explains how a guard protects workers?
  Stops the machine when a worker enters the danger area
  Restrains the worker from entering the danger area
  Creates distance to keep the worker from entering the danger area
  Provides a barrier to prevent access to the danger area
Answer: d. Provides a barrier to prevent access to the danger area

## Slide 54: Knowledge Check
Which of the following is an example of a safeguarding device?
  Protective shield
  Hand-feeding tool
  Safety trip control
  Awareness barrier
Answer: c. Safety trip control